## Slide 1: Cross-Country for Beginners Part 5: Landing Out
Bill Elliott and Rand Baldwin

## Slide 2: Six Week Agenda
  Weather and Preparation (needed skills, glider & instrumentation, biological)
  Thermals and Triggers
  Climbing—and the art of thermaling
  Cruising and In-Flight Decision Making
  Landing Out and Post-Flight Analysis
  Flight Computers and Final Glides

## Slide 3: Personal Equipment
Cell phone
SPOT
Water and food
Survival kit
Extra clothing
Road maps – in case you can’t access Google Maps
Pen and paper
Giveaways – brochures, DVDs, business cards
Book, iPod, etc. to entertain yourself while you await your ever-faithful crew

## Slide 4: Thinking Ahead
“Remember, you fly a glider
with your head, not with your hands.”
- Kai Gertsen, Introduction to Cross Country Soaring -

## Slide 5: Thinking Ahead
“Never let the glider take you somewhere your brain didn’t get to five minutes earlier.”
- Kai Gertsen, Introduction to Cross Country Soaring -

## Slide 6: Decision Heights
At 3,000’ AGL
Start looking for general areas that appear landable. Head in that general direction.
.
By 2,000’
Select a specific field and look for obstacles and hazards. If possible, select an easy alternate in case, as you get lower, you find something wrong with your first choice.
By 1,000’
Commit to land in your chosen field.

## Slide 7: Field Selection Preference
Airport!
Cultivated field (plowed and harrowed)
Young crop
Freshly harvested crop
Newly mowed fields of even texture
Pastures

## Slide 8: Non-Towered Airports
Monitor CTAF when approaching to land
Request airport advisory
Landing pattern
  Use segmented circle if present
  Left-hand pattern if no other info
  Enter at ~1,000’ unless otherwise indicated
Announce on CTAF (usually Unicom)
Watch out for. . .
  Other traffic
  Runway lights
  Steep runway shoulders

## Slide 9: Field Selection: Size and Color
Size
  Best – Large field with no obstructions on the approach end
Color
  Best – Evenly colored brown field
  Next – Light green
  AVOID – Bright yellow and light green
  Straight lines or break in color may indicate a fence or ditch
  Uneven colors – Uneven, rolling terrain

## Slide 10: Field Selection Obstructions and Field Length
Minimum length
  No obstacles on approach: 1,000’
  Obstacles present: 1,500’
  Obstruction at approach end reduces effective field length by 10x the obstruction height
100’
1,500’
500’
Field Length
5:1 Approach
Obstruction
Stopping Distance

## Slide 11: Field Selection: Crop and Slope
Crop
  Good – Freshly cultivated crop
  Good – Freshly harvested crop
  Poor – Rough, mottled texture, rocks
Slope
  Always land uphill regardless of wind!
  A slope that can be perceived from the air is steeper than you think
  Landing uphill – carry a little extra airspeed on the approach

## Slide 12: Field Selection: Wind
Land into wind whenever possible
  But remember: Slope takes precedence!
Know Thy Wind!
  Smoke, dust, water, cattle, flight computer

## Slide 13: “Know Thy Winds!” -- a quote from Gavin Wills --
What is the wind at altitude? How do you know?
  Flight computer
  Drift of glider while thermaling
  Movement of cloud shadows on the ground
What is the wind on the ground? How do you know?
  Smoke from small fires
  Wind signs on the water (ponds)
  Trash moving in a field
Are the winds the same … probably not.
Thermals will cause a distinct shift in the wind direction on the ground so pay attention.

## Slide 14: Field Selection: Livestock
If at all possible, avoid fields containing livestock
  Cattle will walk over the glider, lick it, etc.
  Bulls!! (Ask Francois Pin)

## Slide 15: Serious Hazards
Wires
Fences
Slopes

## Slide 16: Field Selection: Wires
Wires are often invisible
Pole shadows are sometimes visible
NEVER fly under wires
Roads and buildings are often accompanied by wires
Watch for wires leading to buildings inside fields

## Slide 17: Field Selection: Bad…
Water
Swamps
Tall grass or crops
Most roads

## Slide 18: Pop Quiz!
Which of the following describes the best off-field landing site?
  No obstructions, 1,000’ long
  No obstruction on approach, slightly downhill, 1,500’ long
  No obstruction on approach, downwind, 1,200’ long
  100’ obstruction on approach, 1,800’ long

## Slide 19: Pattern and Approach
Check:
Obstructions
Field Condition
Wind
Wind
Continue to
Check Field
Pre-Landing
Checklist
Use 360 degree pattern for all off-field landings
Otherwise, same procedure as at home field

## Slide 20: Common Errors
Not using angles to judge approach
Too close to field on downwind
Turning onto base leg too early
Too high on final
Excessive airspeed (esp. on final approach)
Poor coordination
Forgetting pre-landing checklist

## Slide 21: Landing
Land in the ‘middle’ of the largest field
Pattern speed
  Same as at home given wind and turbulence
Touch down at minimum speed
  Two-point or slightly tail-first touchdown
Stop as soon as possible
In high crops
  Keep wings level and no airbrakes
Never land with the gear retracted
  Unless the POH recommends otherwise

## Slide 22: After Landing
Inspect and secure glider
Get coordinates from flight computer
Call or home and report your position and status to your crew
  Make sure lat and lon are in format crew needs
Use SPOT ‘Help’ function if appropriate
Find landowner if possible
  Take pen, paper, road maps, valuables
Assess field access and plan for trailer routing and disassembly process
Wipe down glider
Remove tape and possibly winglets and stab
If most others are still flying, think about and write down errors you made and how you might have avoided a landout

## Slide 23: Post-Flight Analysis

## Slide 24: Six Week Agenda
  Weather and Preparation (needed skills, glider & instrumentation, biological)
  Thermals and Triggers
  Climbing—and the art of thermaling
  Cruising and In-Flight Decision Making
  Outlanding and Post-Flight Analysis
  Flight Computers and Final Glides